## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 6 “Error Detection and Correction”.

## Slide 2: Error Detection and Correction
Chapter 6
Notes: In earlier chapters, we talked about transmission impairments and the effect
of data rate and signal-to-noise ratio on bit error rate. Regardless of the design
of the transmission system, there will be errors, resulting in the change of one
or more bits in a transmitted block of data.
This chapter examines error-detecting and error-correcting codes. ARQ protocols
are discussed in Chapter 7. After a brief discussion of the distinction between
single-bit errors and burst errors, this chapter describes three approaches to error
detection: the use of parity bits, the Internet checksum technique, and the cyclic
redundancy check (CRC). The CRC error-detecting code is used in a wide variety
of applications. Because of its complexity, we present three different approaches to
describing the CRC algorithm.
For error correction, this chapter provides an overview of the general principles
of error-correcting codes. Specific examples are provided in Chapter 16.

## Slide 3
“Redundancy is a property of languages, codes and sign systems which arises from a superfluity of rules, and which facilitates communication in spite of all the uncertainty acting against it.
Redundancy may be said to be due to an additional set of rules, whereby it becomes increasingly difficult to make an undetectable mistake.”
—On Human Communication,
Colin Cherry
Notes: Three approaches are in common use for coping with data transmission
errors:
• Error-detection codes
• Error-correction codes, also called forward error correction (FEC) codes
• Automatic repeat request (ARQ) protocols
All three approaches are applied to individual blocks of data, called
frames, packets, or cells, depending on the protocol used for data exchange.
The first two approaches, which are the subject of this chapter, use redundancy .
In essence, for error detection and error correction, additional bits, which are
a function of the data bits, are appended to the data bits by the sender. These
redundant bits are used by the receiver for the purpose of error detection or
correction.
An error-detection code simply detects the presence of an error.
Typically, such codes are used in conjunction with a protocol at the data link
or transport level (see Figure 2.3) that uses an ARQ scheme. With an ARQ
scheme, a receiver discards a block of data in which an error is detected and
the transmitter retransmits that block of data. FEC codes are designed not
just to detect but correct errors, avoiding the need for retransmission. FEC
schemes are frequently used in wireless transmission, where retransmission
schemes are highly inefficient and error rates may be high.

## Slide 4: Types of Errors
An error occurs when a bit is altered between transmission and reception
  Binary 1 is transmitted and binary 0 is received
  Binary 0 is transmitted and binary 1 is received
Single bit errors
Isolated error that alters one bit but does not affect nearby bits
Burst errors
Contiguous sequence of B bits in which the first and last bits and any number of intermediate bits are received in error
Can occur in the presence of white noise
Can be caused by impulse noise or by fading in a mobile wireless environment
Effects of burst errors are greater at higher data rates
Notes: In digital transmission systems, an error occurs when a bit is altered between transmission
and reception; that is, a binary 1 is transmitted and a binary 0 is received,
or a binary 0 is transmitted and a binary 1 is received. Two general types of errors
can occur: single-bit errors and burst errors. A single-bit error is an isolated error
condition that alters one bit but does not affect nearby bits. A burst error of length
B is a contiguous sequence of B bits in which the first and last bits and any number
of intermediate bits are received in error. More precisely, IEEE Std 100 and ITU-T
Recommendation Q.9 both define an error burst as follows:
Error burst: A group of bits in which two successive erroneous bits are
always separated by less than a given number x of correct bits. The last
erroneous bit in the burst and the first erroneous bit in the following burst
are accordingly separated by x correct bits or more.

## Slide 5
Notes: Thus, in an error burst, there is a cluster of bits in which a number of errors
occur, although not necessarily all of the bits in the cluster suffer an error. Figure 6.1
provides an example of both types of errors.
A single-bit error can occur in the presence of white noise, when a slight random
deterioration of the signal-to-noise ratio is sufficient to confuse the receiver’s
decision of a single bit. Burst errors are more common and more difficult to deal
with. Burst errors can be caused by impulse noise, which was described in Chapter 3.
Another cause is fading in a mobile wireless environment; fading is described in
Chapter 10.
Note that the effects of burst errors are greater at higher data rates.

## Slide 6: Error Detection
Regardless of design you will have errors, resulting in the change of one or more bits in a transmitted frame
Frames
  Data transmitted as one or more contiguous sequences of bits
The probability that a frame arrives with no bit errors decreases when the probability of a single bit error increases
The probability that a frame arrives with no bit errors decreases with increasing frame length
  The longer the frame, the more bits it has and the higher the probability that one of these is in error
Pb
P1
P2
P3
Probability that a bit is received in error; also known as the bit error rate (BER)
Probability that a frame arrives with no bit errors
Probability that, with an error-detecting algorithm in use, a frame arrives with one or more undetected errors
Probability that, with an error-detecting algorithm in use, a frame arrives with one or more detected bit errors but no undetected bit errors
Notes: Regardless of the design of the transmission system, there will be errors, resulting in
the change of one or more bits in a transmitted frame. In what follows, we assume
that data are transmitted as one or more contiguous sequences of bits, called frames.
We define these probabilities with respect to errors in transmitted frames:
Pb : Probability that a bit is received in error; also known as the bit error rate
(BER)
P1 : Probability that a frame arrives with no bit errors
P2 : Probability that, with an error-detecting algorithm in use, a frame arrives with
one or more undetected errors
P3 : Probability that, with an error-detecting algorithm in use, a frame arrives
with one or more detected bit errors but no undetected bit errors
The probability that a frame
arrives with no bit errors decreases when the probability of a single bit error
increases, as you would expect. Also, the probability that a frame arrives with no bit
errors decreases with increasing frame length; the longer the frame, the more bits it
has and the higher the probability that one of these is in error.

## Slide 7
Notes: This is the kind of result that motivates the use of error-detecting techniques
to achieve a desired frame error rate on a connection with a given BER. All of these
techniques operate on the following principle (Figure 6.2). For a given frame of bits,
additional bits that constitute an error-detecting code are added by the transmitter.
This code is calculated as a function of the other transmitted bits. Typically, for a
data block of k bits, the error-detecting algorithm yields an error-detecting code of
n - kbits, where (n - k ) <k. The error-detecting code, also referred to as the check
bits, is appended to the data block to produce a frame of n bits, which is then transmitted.
The receiver separates the incoming frame into the k bits of data and (n - k )
bits of the error-detecting code. The receiver performs the same error-detecting
calculation on the data bits and compares this value with the value of the incoming
error-detecting code. A detected error occurs if and only if there is a mismatch.
Thus P3 is the probability that a frame contains errors and that the error-detecting
scheme will detect that fact. P2 is known as the residual error rate and is the probability
that an error will be undetected despite the use of an error-detecting scheme.

## Slide 8: Parity Check
The simplest error detecting scheme is to append a parity bit to the end of a block of data
  If any even number of bits are inverted due to error, an undetected error occurs
Even parity
Even number of 1s
Used for synchronous transmission
Odd parity
Odd number of 1s
Used for asynchronous transmission
Notes: The simplest error-detecting scheme is to append a parity bit to the end of a block of data. The value of this bit is selected so that the character has an even number of 1s (even parity) or an odd number of 1s (odd parity). Note, however, that if two (or any even number) of bits are inverted due to error, an undetected error occurs. Typically, even parity is used for synchronous transmission and odd parity for asynchronous transmission. The use of the parity bit is not foolproof, as noise impulses are often long enough to destroy more than one bit, particularly at high data rates.

## Slide 9
Notes: The two-dimensional parity scheme, illustrated in Figure 6.3, is more robust than
the single parity bit. The string of data bits to be checked is arranged in a two-dimensional
array. Appended to each row i is an even parity bit ri for that row, and appended to each column j is an even parity bit cj for that column. An overall
parity bit p completes the matrix. Thus the error-detecting code consists of i + j + 1
parity bits.
In this scheme, every bit participates in two parity checks. As with a simple
parity bit, any odd number of bit errors is detected.
Figure 6.3b shows a string of 20 data bits arranged in a 4 * 5
array, with the parity bits calculated, to form a 5 * 6 array. When a single-bit
error occurs in Figure 6.3c, both the corresponding row and column parity bits
now indicate an error. Furthermore, the error can be determined to be at the
intersection of that row and column. Thus it is possible to not only detect but
also correct the bit error.
If an even number of errors occur in a row, the errors are detected by the
column parity bits. Similarly, if an even number of errors occur in a column,
the errors are detected by the row parity bits. However, any pattern of four
errors forming a rectangle, as shown in Figure 6.3d, is undetectable. If the four
circled bits change value, the corresponding row and column parity bits do not
change value.

## Slide 10: The Internet Checksum
Error detecting code used in many Internet standard protocols, including IP, TCP, and UDP
Ones-complement operation
  Replace 0 digits with 1 digits and 1 digits with 0 digits
Ones-complement addition
  The two numbers are treated as unsigned binary integers and added
  If there is a carry out of the leftmost bit, add 1 to the sum (end-around carry)
Notes: The Internet checksum is an error-detecting code used in many Internet standard
protocols, including IP, TCP, and UDP. The calculation makes use of the
ones-complement operation and ones-complement addition. To perform the ones-complement
operation on a set of binary digits, replace 0 digits with 1 digits and
1 digits with 0 digits. The ones-complement addition of two binary integers of equal
bit length is performed as follows:
1. The two numbers are treated as unsigned binary integers and added.
2. If there is a carry out of the leftmost bit, add 1 to the sum. This is called an end-around
carry.
Typically, the checksum is included as a field in the header of a protocol data
unit, such as in IP datagram. To compute the checksum, the checksum field is first
set to all zeros. The checksum is then calculated by performing the ones-complement
addition of all the words in the header, and then taking the ones-complement operation
of the result. This result is placed in the checksum field.
To verify a checksum, the ones-complement sum is computed over the same
set of octets, including the checksum field. If the result is all 1 bits (- 0 in ones-complement
arithmetic), the check succeeds.

## Slide 11
Notes: Figure 6.4a shows the results of the calculation. Thus, the transmitted packet
is 00 01 F2 03 F4 F5 F6 F7 0D. Figure 6.4b shows the calculation carried out by
the receiver on the entire data block, including the checksum. The result is a
value of all ones, which verifies that no errors have been detected.
The Internet checksum provides greater error-detection capability than a parity
bit or two-dimensional parity scheme but is considerably less effective than the
cyclic redundancy check (CRC), discussed next. The primary reason for its adoption
in Internet protocols is efficiency. Most of these protocols are implemented
in software and the Internet checksum, involving simple addition and comparison
operations, causes very little overhead. It is assumed that at the lower link level, a
strong error-detection code such as CRC is used, and so the Internet checksum is
simply an additional end-to-end check for errors.

## Slide 12: Cyclic Redundancy Check
one of most common and powerful checks
for a block of k bits transmitter generates an n bit frame check sequence (FCS)
transmits k+n bits which is exactly divisible by some number
receiver divides frame by that number
  if no remainder, assume no error
  for math, see Stallings chapter 6
Notes: One of the most common, and one of the most powerful, error-detecting codes is the cyclic redundancy check (CRC), which can be described as follows. Given a k-bit block of bits, or message, the transmitter generates an (n – k)-bit sequence, known as a frame check sequence (FCS), such that the resulting frame, consisting of n bits, is exactly divisible by some predetermined number. The receiver then divides the incoming frame by that number and, if there is no remainder, assumes there was no error. Can state this procedure in three equivalent ways: modulo 2 arithmetic, polynomials, and digital logic, as detailed in Stallings DCC8e chapter 6.3. Comes down to working out what remainder exists when divide data by desired number, and using that as the FCS value appended tot eh data to form the block.

## Slide 13: CRC Process
Modulo 2 arithmetic
  Uses binary addition with no carries
  An example is shown on page 218 in the textbook
Polynomials
  Express all values as polynomials in a dummy variable X, with binary coefficients
  Coefficients correspond to the bits in the binary number
  An example is shown on page 221 in the textbook
Digital logic
  Dividing circuit consisting of XOR gates and a shift register
  Shift register is a string of 1-bit storage devices
  Each device has an output line, which indicates the value currently stored, and an input line
  At discrete time instants, known as clock times, the value in the storage device is replaced by the value indicated by its input line
  The entire register is clocked simultaneously, causing a 1-bit shift along the entire register
  An example is referenced on page 223 in the textbook
Notes: Modulo 2 arithmetic uses binary addition with no carries, which is just the exclusive-
OR (XOR) operation. Binary subtraction with no carries is also interpreted as the
XOR operation.
A second way of viewing the CRC process is to express all values as polynomials
in a dummy variable X, with binary coefficients. The coefficients correspond to the
bits in the binary number.
The CRC process can be represented by, and indeed implemented as, a dividing
circuit consisting of XOR gates and a shift register. The shift register is a string
of 1-bit storage devices. Each device has an output line, which indicates the value
currently stored, and an input line. At discrete time instants, known as clock times,
the value in the storage device is replaced by the value indicated by its input
line. The entire register is clocked simultaneously, causing a 1-bit shift along the
entire register.

## Slide 14: Modulo 2 Arithmetic (XOR)
Define:
  T = (k+n)-bit frame to be transmitted, n < k
  M = k-bit message, the first k bits of T
  F = n-bit FCS, the last n bits of T
  P = pattern of n+1 bits, the predetermined divisor
We would like T/P to have no remainder
  T = 2nM + F
  2nM/P = Q + R/P, R is at least one bit less than P
  Use R as the FCS (i.e. F), i.e. T = 2nM + R
  Examine if T/P have no remainder?
    T/P = (2nM + R)/P = Q + R/P + R/P = Q + (R+R)/P = Q

## Slide 15: Modulo 2 Arithmetic (cont)
Occurrence of errors
  Tr = T + E
  T = transmitted frame
  E = error pattern with 1s in positions of error
  Tr = received frame
Fail to detect an error if and only if Tr is divisible by P
  i.e. if and only if E is divisible by P

## Slide 16
Notes: Figure 6.5 shows the polynomial division that corresponds to the
binary division in the preceding example.

## Slide 17
Notes: The architecture of a CRC circuit is best explained by first considering
an example, which is illustrated in Figure 6.6.
Figure 6.6a shows the shift-register implementation. The process begins with
the shift register cleared (all zeros). The message, or dividend, is then entered
one bit at a time, starting with the most significant bit. Figure 6.6b is a table that
shows the step-by-step operation as the input is applied one bit at a time. Each
row of the table shows the values currently stored in the five shift-register elements.
In addition, the row shows the values that appear at the outputs of the
three XOR circuits. Finally, the row shows the value of the next input bit, which
is available for the operation of the next step.

## Slide 18
Notes: Figure 6.7 indicates the general architecture of the shift-register implementation
of a CRC for a polynomial.

## Slide 19: Forward Error Correction
Correction of detected errors usually requires data blocks to be retransmitted
Not appropriate for wireless applications:
  The bit error rate (BER) on a wireless link can be quite high, which would result in a large number of retransmissions
  Propagation delay is very long compared to the transmission time of a single frame
Need to correct errors on basis of bits received
Codeword
On the transmission end each k-bit block of data is mapped into an n-bit block (n > k) using a forward error correction (FEC) encoder
Notes: Error detection is a useful technique, found in data link control protocols, such as
HDLC, and in transport protocols, such as TCP. As explained in Chapter 7, an error-detecting
code can be used as part of a protocol that corrects errors in transmitted
data by requiring the blocks of data be retransmitted. For wireless applications this
approach is inadequate for two reasons:
1. The BER on a wireless link can be quite high, which would result in a large
number of retransmissions.
2. In some cases, especially satellite links, the propagation delay is very long compared
to the transmission time of a single frame. The result is a very inefficient
system. As is discussed in Chapter 7, the common approach to retransmission
is to retransmit the frame in error plus all subsequent frames. With a long data
link, an error in a single frame necessitates retransmitting many frames.
Instead, it would be desirable to enable the receiver to correct errors in an
incoming transmission on the basis of the bits in that transmission. Figure 6.8 shows
in general how this is done. On the transmission end, each k -bit block of data is
mapped into an n -bit block (n>k) called a codeword , using an FEC (forward
error correction) encoder. The codeword is then transmitted.

## Slide 20
Notes: During transmission, the signal is subject to impairments, which may produce bit errors in the signal. At the receiver, the incoming signal is demodulated to produce a bit string that is similar to the original codeword but may contain errors. This block is passed through an FEC decoder, with one of four possible outcomes:
• No errors: If there are no bit errors, the input to the FEC decoder is identical
to the original codeword, and the decoder produces the original data block as
output.
• Detectable, correctable errors: For certain error patterns, it is possible for the
decoder to detect and correct those errors. Thus, even though the incoming
data block differs from the transmitted codeword, the FEC decoder is able to
map this block into the original data block.
• Detectable, not correctable errors: For certain error patterns, the decoder can
detect but not correct the errors. In this case, the decoder simply reports an
uncorrectable error.
• Undetectable errors: For certain, typically rare, error patterns, the decoder
does not detect the error and maps the incoming n-bit data block into a k-bit
block that differs from the original k-bit block.

## Slide 21: Block Code Principles
Hamming distance
  d(v1, v2) between two n–bit binary sequences v1 and v2 is the number of bits in which v1 and v2 disagree
  See example on page 227 in the textbook
Redundancy of the code
  The ratio of redundant bits to data bits (n-k)/k
Code rate
  The ratio of data bits to total bits k/n
  Is a measure of how much additional bandwidth is required to carry data at the same data rate as without the code
  See example on page 229 in the textbook
Notes: To begin, we define a term that shall be of use to us. The Hamming distance d(v1 , v2)
between two n -bit binary sequences v1 and v2 is the number of bits in which v1 and
v2 disagree.
With an (n, k ) block code, there are 2k valid codewords out of a total of 2n
possible codewords. The ratio of redundant bits to data bits, 1n - k2 /k , is called
the redundancy of the code, and the ratio of data bits to total bits, k /n, is called
the code rate . The code rate is a measure of how much additional bandwidth is
required to carry data at the same data rate as without the code. For example, a
code rate of 1/2 requires double the transmission capacity of an uncoded system to
maintain the same data rate. Our example has a code rate of 2/5 and so requires
2.5 times the capacity of an uncoded system. For example, if the data rate input
to the encoder is 1 Mbps, then the output from the encoder must be at a rate of
2.5 Mbps to keep up.

## Slide 22
Notes: It is instructive to examine Figure 6.9. The literature on error-correcting codes
frequently includes graphs of this sort to demonstrate the effectiveness of various
encoding schemes.
In Figure 6.9, the curve on
the right is for an uncoded modulation system. To the left of that curve is the area in
which improvement can be achieved.

## Slide 23: Summary
Types of errors
Error detection
Parity check
  Parity bit
  Two-dimensional parity check
Internet checksum
Cyclic redundancy check
  Modulo 2 arithmetic
  Polynomials
  Digital logic
Forward error correction
  Block code principles
Notes: Chapter 6summary.